## Slide 1: Part 1: Introduction to wireless networking management
Paola Soto and Miguel Camelo

## Slide 2: Introduction to Wi – Fi

## Slide 3: Wi-Fi Background
Technically known as IEEE802.11 (back in 1999).
Mainly uses the 2.4GHz and the 5GHz radio spectrum bands (a.k.a. unlicensed spectrum).
The spectrum is shared with other technologies.
  Listen before talk mechanisms – spectrum sensing
Introduction
Source: https://terasense.com/terahertz-technology/radio-frequency-bands/

## Slide 4: Wi-Fi Background
Through protocols Wi-Fi shares the spectrum with same/other technologies.
Carrier Sense Multiple Access/Collision Avoidance (CSMA/CA)
Spectrum Sharing in Wi-Fi
Source: https://en.wikipedia.org/wiki/Carrier-sense_multiple_access_with_collision_avoidance
Source: https://www.engeniustech.com/go-guide-channel-transmit-power-wi-fi-networks-2/
Notes: For each transmission, the sender sense the transmission medium to identify if it’s idle or not. If the transmission medium is not idle, the sender will hold its transmission for a random period of time (Backoff).  Carrier Sense (CS)
The CS will continue until the medium is free to transmit.
Even if the medium is sensed idle, the transmission can cause collisions (see the hidden node problem). For newer versions of Wi-Fi, a Request To Send (RTS) is sent to the AP. The station only sends data when it receives a Clear To Send (CTS) message.

## Slide 5: Introduction to Channel Bonding

## Slide 6: Channel Bonding
Typical bandwidth in Wi-Fi is 20MHz
Key Idea: Improve capacity by bonding frequency channels
CSMA/CA is still valid.
Can have different channel access policies
Increase available bandwidth
Source: https://www.engeniustech.com/go-guide-channel-transmit-power-wi-fi-networks-2/
Notes: Typically, Wi-Fi transmissions occupy 20MHz bandwidth. However, with channel bonding, two or more adjacent channels can be used for transmission. This increases the allocated bandwidth per transmission and more data can be transmitted per unit of time.
In this case, the CSMA/CA mechanism will check the medium only in the primary channel.

## Slide 7: Channel Bonding
Increase available bandwidth
1. F. Wilhelmi, D. Goez, P. Soto, et al, “Machine learning for performance prediction of channel bonding in next-generation IEEE 802.11 WLANs”, ITU Journal on Future and Evolving Technologies, Volume 2 (2021), Issue 4 - AI and machine learning solutions in 5G and future networks, Pages 67-79.
Dynamic Access Policy
Notes: Typically, Wi-Fi transmissions occupy 20MHz bandwidth. However, with channel bonding, two or more adjacent channels can be used for transmission. This increases the allocated bandwidth per transmission and more data can be transmitted per unit of time.
In this case, the CSMA/CA mechanism will check the medium only in the primary channel.
If you are the only station that is transmitting, then the solution for improved throughput is trivial, just select the higher number of channels to be bonded, so you have higher bandwidth to transmit. But this is not always possible due to the CSMA algorithm.
With CSMA, the station is only able to transmit when your allocated channels are sensed free. Depending on the policy your AP is configured to follow, this may lead to problems like starvation, because of the lack of coordination between devices.

## Slide 8: Channel Bonding
Challenges
1 |  |  |  |  |  |  | 
Channel(s): 1
APA
STAA
Source: https://www.itu.int/en/ITU-T/AI/challenge/2020/Documents/ITU%20AI_ML%20Challenge%20-%20UPF.pdf
Throughput: 20Mbps
RSSI: -67dBm
The quality of the transmission (e.g., throughput, delay) depends on the Tx power & Channel effects
C: Channel capacity
B: Channel bandwith
SINR: signal to interference plus noise ratio
Notes: There is a tradeoff between the channel width, the data rate (determined by your modulation scheme) and the contention (gain access to the medium). Then, the more bandwidth you have, the more channel capacity, but at the same time, the more interference, the less the channel capacity.
The transmission power is spread over the multiple channels, so, the more channels you can bond, the more bandwidth, and therefore, the more channel capacity.
Let’s assume that we only have a WLAN (BSS – Basic Service Set) that is using only channel ine. Let’s say that with the RSSI (signal strenght) referenced here, the STA can achieve a throughput of 20Mbps.

## Slide 9: Channel Bonding
Challenges
1 | 2 | 3 | 4 | 5 | 6 | 7 | 8
Channel(s): 1-8
APA
STAA
Source: https://www.itu.int/en/ITU-T/AI/challenge/2020/Documents/ITU%20AI_ML%20Challenge%20-%20UPF.pdf
Throughput: 60Mbps
RSSI: -80dBm
The throughput is not x8 since the transmission power is spread over the spectrum
Notes: There is a tradeoff between the channel width, the data rate (determined by your modulation scheme) and the contention (gain access to the medium). Then, the more bandwidth you have, the more channel capacity, but at the same time, the more interference, the less the channel capacity.
The transmission power is spread over the multiple channels, so, the more channels you can bond, the more bandwidth, and therefore, the more channel capacity.
Let’s assume that we only have a WLAN (BSS – Basic Service Set) that is using only channel ine. Let’s say that with the RSSI (signal strenght) referenced here, the STA can achieve a throughput of 20Mbps.
However, if the STA is located a little bit further away, having an RSSI of -80dBm the throuhput is not necessarly eight times the previous throughput. Since the power is lower, the modulation that it needs to use is having a lower datarate and therefore the throughput is not as expected.
The situation is worsened if you have more devices and more WLANs in the area.
So ideally, the APs should have a way to predict their expected throughput using a given configuration.
It is clear that channel bonding is a combinatorial state space problem where analytical models and Markov models will fail due to the higher complexity.

## Slide 10: Digital Twins

## Slide 11: Digital Twins
Digital representation of a physical element.
Monitored data to enhance the operational view of the physical system.
Typically employs Machine Learning and Artificial Intelligence in its construction.
Applied to networks, a Digital Twin it’s a network model.
  What-if analysis  What is the obtained throughput under this configuration?
  Network planning and optimization  Can the network support another demand?
Introduction
Source: https://www.motioncontroltips.com/what-are-digital-twins-how-are-they-used-in-industrial-manufacturing/

## Slide 12: Digital Twins
Why a NDT is needed in next generation WLANs?
Controller
(1). Measurements
(e.g., network state)
(1). Measurements
(e.g., network state)
(4). Channel
Configurations
Network Digital Twin
(3). Expected performance
(2). Set of configurations to evaluate
Notes: Network models and optimization algorithms are developed for assisting network providers to configure the network. In this way, network administrators set an intent (e.g., maximize the throughput) as input to the optimization algorithm, and through the model, the algorithm finds the network configuration that fulfils the requirements.
Ideally, future networks will offer a high degree of automation and this process could be completely automatic without human intervention. How? By having an accurate network digital twin that can analyse in real-time, the data received from the network.
Several techniques can be used to build that network digital twin, but the most promising ones are based in AI and ML.
Firstly, different measurements are constantly collected from the network and delivered to the controller. The collected measurements constitute the network state. The measuring time depends on the kind of decision that is being optimized. For instance, long-term metrics, such as energy consumption, do not require short monitoring intervals. Although some of the features are difficult to get, we expect that the introduction of Software Defined Networking (SDN) in wireless networks will facilitate the data collection campaigns, where the collected data can later be used for intelligent management decisions.
Then, the evaluation of different configurations will be executed in a timely manner if a triggering condition is met, forming a closed control-loop, for example, if the controller perceives that 50% of their managed devices have lower throughput than expected. In this case, the ML model will generate a prediction for every evaluated configuration. Note that a traditional model (e.g., Markov model) takes a long time to generate a prediction, longer than the time required to optimize the spectrum usage to decrease interference and improve the user experience