## Slide 1: Part 3: Building an NDT for Next-Generation WLANs with Graph Neural Networks (GNNs)
Paola Soto and Miguel Camelo

## Slide 2: Why GNNs
GNNs are good working with relational data
Source: https://thetechbrook.com/inside-the-black-box-of-ai/
Notes: Relational data: one sample relates to another
Extra information is carried in the topology of the graph.
Why relational data cannot be handled by CNNs? Because of its arbitrary size.

## Slide 3: Different Neural Networks
Type of NN | Information structure
Fully Connected | Arbitrary
Convolutional | Spatial
Recurrent | Sequential
Graph | Relational
Source: https://neptune.ai/blog/graph-neural-network-and-some-of-gnn-applications
Molecules

## Slide 4: Introduction to GNNs

## Slide 5: What is a graph?
A graph is 2-tuple G=(V, E) where V are the nodes and E are the links.
Each node has its own set of features.
Optionally, each link has its own set of features
Source: https://www.freecodecamp.org/news/graph-neural-networks-explained-with-examples/

## Slide 6: How GNNs work?
Adjacency matrix: a mathematical way to express the graph.
Exploit locality information.
Order-invariant aggregators
  Sum
  Average
  Maximum
Aggregating information – Message passing
Source: https://neptune.ai/blog/graph-neural-network-and-some-of-gnn-applications
Notes: The information carried by a node’s neighbohr affects the implicated node.
We need to aggregate the information from k hops to the k-1 hop.

## Slide 7: GNNs for solving topology-based problems

## Slide 8: GNNs applied to WLANs
AP A
Pos: (10, 10)
AP B
Pos: (20, 10)
STA A1
Pos: (9.5, 15)
STA B1
Pos: (22.3, 11)
RSSI = -44dBm
Interference = -87dBm
Channels: [0,1]
Channels: [0,3]
Access Point (AP)
Station (STA)
AP-AP Link
AP-STA Link
3
1
4
2
5
8
6
9
10
7

## Slide 9: GNNs
GNB3: Graph Neural Block
  Node attributes: node type, x-y coordinate, channel configuration
    AP: mean airtime,
    STA: SINR
  Edge attributes: edge type, distance
    AP-AP: interference
    AP-STA: RSSI
  Architecture
    Node model
    Edge model
Basic Model
Access Point (AP)
Station (STA)
AP-AP Link
AP-STA Link
3. P. W. Battaglia et al., “Relational inductive biases, deep learning, and graph networks,”, arXiv preprint arXiv:1806.01261, 2018

## Slide 10: Hands – On

## Slide 11: Link
Notebook: Building an NDT for next-generation WLANs using GNNs